## Slide 1
Australian Geospatial Reference System
Webinar Series
Webinar 2: Geocentric Datum of Australia 2020
Nicholas Brown
Director of National Geodesy
Geoscience Australia
Chair of ICSM Permanent Committee on Geodesy
@nich0lasbr0wn

## Slide 2
www.sli.do #AGRS
www.sli.do
#AGRS

## Slide 3: Who am I?
Director of National Geodesy at Geoscience Australia
Commonwealth representative on Intergovernmental Committee on Surveying and Mapping (ICSM)
Chair of the ICSM Permanent Committee on Geodesy (PCG)
Australian representative on FIG Commission 5 – Positioning and Measurement
Favourite geodesist - Copernicus
www.sli.do #AGRS

## Slide 4
Australian Plate Motion Model
7 cm/yr
Geocentric Datum of Australia 2020
Geocentric Datum of Australia 1994
Transformation parameters / grids
Δ 1.8 m
Australian Terrestrial Reference Frame
ATRF
GDA2020
GDA94
Australian Quasigeoid Model
Australian Height Datum
AHD
AUSGeoid2020
AUSGeoid09
σ = 1-8 cm
σ = 6-13 cm
σ = ?
Australian Vertical Working Surface
AVWS
Webinar 2: GDA2020
Webinar 3: ATRF
Webinar 4: Height
Notes: PCG ensures Australia and New Zealand have the geospatial reference systems *including datums, reference frames, working surfaces, and standards to meet user needs.
It’s complex – yes – but as we try to measure things more accurately, we need to ensure we have the grs to enable those applications.

## Slide 5
shape
gravity field
orientation
Geodesy
noun
Science of measuring the shape, orientation and gravity field of the Earth and how it changes over time.
Geodesist
noun
Magical creatures who create and maintain the Geospatial Reference System.
Geospatial Reference System
noun
Collection of datums, infrastructure, models and standards required for 4D positioning.
www.sli.do #AGRS
Notes: Geodesy – read off screen,
GRS - explain there are geometric and physical components of a GRS

## Slide 6
Accuracy
3-10 cm
www.sli.do #AGRS

## Slide 7
The cumulative distribution of global core revenue (value of GNSS chipsets) projected by the European GNSS Agency (GSA, 2015) for the period 2013 – 2023.
Traditional markets make up <10% of GNSS chipset sales
Significant growth in new markets:
Location Based Services
Intelligent Transport
www.sli.do #AGRS
GNSS chipset sales (2013-2023)

## Slide 8: Why couldn’t GDA94 meet user requirements?
Positions from GNSS satellites do not match data on GDA94
Offset from GNSS: ~1.8 m (~7 cm / plate tectonic motion
Spatial data can’t be aligned for good decision making
We aren’t capitalising on the benefits of precise positioning
Positions from GNSS satellites do match data on GDA2020
Offset from GNSS: 0 m on 1/1/2020
Spatial data is aligned at 10 cm level for improved decision making
Geocentric Datum of Australia 1994
GDA94
GDA2020
Geocentric Datum of Australia 2020
www.sli.do #AGRS

## Slide 9: Why couldn’t GDA94 meet user requirements?
Motion of the Australian Plate
Australia is the fastest moving continental plate (~7 cm/yr NNE)
GNSS provides coordinates in ITRF (position of Australian plate now)
Users will soon see a ~1.8 m mismatch between GNSS positions and spatial datasets (if in GDA94)
Why not just transform it back to 1994? …
www.sli.do #AGRS

## Slide 10
www.sli.do #AGRS
GDA94 = ITRF1992@1994.0
~7 cm / yr
ITRF1992@1995.0 (~7 cm NNE of 1994)
Updates to ITRF; 1994, 1996, 1997, 2000, 2005, 2008, 2014.
Each is an improved realisation of the shape of the Earth
+
+
GDA2020 = ITRF2014@2020
ITRF2014 coordinates are different to ITRF1992 coordinates
e.g. heights are 9 cm different
+
7 parameter
transformation
Why don’t they match?
Changes in the reference frame between the ITRF1992 and today
Local distortions (e.g. subsidence, earthquakes)
Lack of rigour in the way GDA94 coordinates were computed

## Slide 11
Why couldn’t GDA94 meet user requirements?
GDA94
Adjustments
2. Distortion in GDA94
Changes in the reference frame between the ITRF1992 and today
Local distortions (e.g. subsidence, earthquakes)
Lack of rigour in the way GDA94 coordinates were computed
ITRF1992 @ 1994.0
Updated to 21 points in April 2012
www.sli.do #AGRS
Notes: These vectors show the offset between GDA94 as established in 1997 compared to ITRF coordinates observed in 2010 transformed back to 1994
Majority of errors in the order of 10 – 20 cm but extend to 30 cm.
local distortions (e.g. subsidence, surface heave)
poor uncertainty propagation down to the marks in the original adjustment (particularly around relative uncertainty)
changes in the reference frame between the ITRF 1992 and today
The implications for errors introduced for big data surveys like LiDAR start to become relevant. When assessing data, how do you know whether the uncertainty is in the survey data or in the datum?

## Slide 12
Source: Joel Haasdyk and Tony Watson, LPI NSW, APAS Conference 2013
Why couldn’t GDA94 meet user requirements?
www.sli.do #AGRS
2. Distortion in GDA94
Changes in the reference frame between the ITRF1992 and today
Local distortions (e.g. subsidence, earthquakes)
Lack of rigour in the way GDA94 coordinates were computed
Notes: These vectors show the offset between GDA94 as established in 1997 compared to ITRF coordinates observed in 2010 transformed back to 1994
Majority of errors in the order of 10 – 20 cm but extend to 30 cm.
local distortions (e.g. subsidence, surface heave)
poor uncertainty propagation down to the marks in the original adjustment (particularly around relative uncertainty)
changes in the reference frame between the ITRF 1992 and today
The implications for errors introduced for big data surveys like LiDAR start to become relevant. When assessing data, how do you know whether the uncertainty is in the survey data or in the datum?

## Slide 13: Building GDA2020
APREF
ITRF2014
2017 RVS Determination
GDA2020
4. Provide access
Rigorous national adjustment (all GNSS and terrestrial observations were used in the same adjustment)
  ~2 million observations
  ~250,000 stations
GNSS Campaign Data
Jurisdictional archive
+
+
1. Start global
Link to the global reference frame
20 GNSS stations in Australia
2. Increase density
Asia-Pacific Reference Frame (Regional reference frame)
454 GNSS stations
3. Legal Determination of ‘Datum’
109 sites in Australia
  Coordinates
  Velocities
  Uncertainties
  Equation to propagate coordinates over time
www.sli.do #AGRS
+
access
constraint

## Slide 14: International Terrestrial Reference Frame 2014
www.sli.do #AGRS

## Slide 15: Asia Pacific Reference Frame (APREF)
Denser regional reference frame
GNSS CORS from the Asia-Pacific region
454 stations
www.sli.do #AGRS

## Slide 16: 2017 RVS Determination (109 subset of APREF)
Criteria for RVS
Operated by Geoscience Australia, state, or territory;
Located on the Australian Tectonic Plate, within Australia’s jurisdiction and on a high quality survey monument; and
Have residuals less than 1 mm/yr relative to plate motion
70 mm/year
57 mm/year
69 mm/year
70 mm/year
60 mm/year
www.sli.do #AGRS

## Slide 17
GDA2020 Determination made in October 2017
Legal Determination of coordinates, velocities and uncertainties of 109 reference sites
Equation permits propagation of coordinates over time
www.sli.do #AGRS
Notes: PCG proposed the development of a new national datum – GDA2020

## Slide 18: Building GDA2020
APREF
ITRF2014
2017 RVS Determination
GDA2020
4. Provide access
Rigorous national adjustment (all GNSS and terrestrial observations were used in the same adjustment)
  ~2 million observations
  ~250,000 stations
GNSS Campaign Data
Jurisdictional archive
+
+
1. Start global
Link to the global reference frame
20 GNSS stations in Australia
2. Increase density
Asia-Pacific Reference Frame (Regional reference frame)
454 GNSS stations
3. Legal Determination of ‘Datum’
109 sites in Australia
  Coordinates
  Velocities
  Uncertainties
  Equation to propagate coordinates over time
www.sli.do #AGRS
+
access
constraint

## Slide 19: GNSS Campaign Data
Ground marks, not Continuously Operating Reference Stations
6+ hour GNSS observations
Input in the national adjustment as ‘baselines’
Not constraint in the adjustment, just measurements
www.sli.do #AGRS

## Slide 20: Jurisdictional Archive
Ground marks, not Continuously Operating Reference Stations
<6 hour GNSS observations
Terrestrial observations
Input in the national adjustment as ‘baselines’
Not constraint in the adjustment, just measurements
www.sli.do #AGRS

## Slide 21: DynAdjust – Open Source – it’s FREE!
www.sli.do #AGRS
https://github.com/icsm-au/DynAdjust

## Slide 22
measurements
1. APREF
2. Campaign
3. Jurisdiction
www.sli.do #AGRS

## Slide 23
Differences | GDA94 | GDA2020
Adjustment approach | State-based, non-contiguous | National
Constraint | AFN, ANN, Marks | CORS solution
Courtesy of Alex Woods, DELWP
www.sli.do #AGRS
GDA94
GDA2020

## Slide 24: GDA2020 Products and Tools
Transformations from GDA94 to GDA2020
  7 parameter transformation (3D)
  NTv2 grids (2D)
    Conformal
    Conformal + Distortion
  Spreadsheet (3D)
  Coordinate transformation web service (based on FME) (2D / 3D)
AUSGeoid2020
GDA2020 Technical Manual
Fact sheets and help guides
www.sli.do #AGRS
https://www.icsm.gov.au/datum/gda-transformation-products-and-tools

## Slide 25: GDA94 – GDA2020 Transformation Parameters
Use common points from GDA94 Determination and GDA2020 Determination
21 reference points from GDA94 AFN minus MAC1, COCO and XMIS due to seismic displacement
Input the coordinates for 18 sites common to GDA94 and GDA2020
Solve for the 7-parameters (3 x rotation, 1 x scale and 3 x translation) using CATREF software
www.sli.do #AGRS

## Slide 26: GDA94 – GDA2020 7 Parameter Transformation
GDA2020 Technical Manual
Convert coordinates from Lat, Long, Ht to X Y Z
Apply this transformation
Convert coordinates from X Y Z to Lat, Long, Ht
3D transformation – deals with 9 cm difference between ITRF1992 and ITRF2014
www.sli.do #AGRS

## Slide 27: GDA94 – GDA2020 7 Parameter Transformation
www.sli.do #AGRS

## Slide 28: GDA94 – GDA2020 NTv2 Conformal Transformation Grid
Grid representation of 7 parameter conformal transformation
Application:
2D data
Data not influenced by the survey control mark network - GNSS only
Courtesy of Alex Woods, DELWP
www.sli.do #AGRS
1.739 m
1.816 m
1.802 m
1.702 m
1.496 m
1.638 m
1.553 m

## Slide 29: Euler Pole

## Slide 30: GDA94 – GDA2020 NTv2 Conformal + Distortion Transformation Grid
Input:
Conformal grid
Survey marks
  Published GDA94
  Adjusted GDA2020
Application:
2D
Data aligned with survey control mark network
Courtesy of Alex Woods, DELWP
www.sli.do #AGRS

## Slide 31
conformal (green) and distortion (red) components of the transformation grids;
low reliability of distortion component;
the grid has a latitude component and longitude component.
GDA94 – GDA2020 NTv2 Conformal + Distortion Transformation Grid
www.sli.do #AGRS

## Slide 32: Choice of transformation tool
Specific jurisdictional advice supplied in GDA2020 Technical Manual
If in doubt contact your state / territory land survey authority
Transformation Option | Data | Coordinates
7 parameter | Recommended for users transforming from GDA94 coordinates derived from CORS | 3D
Conformal grid | Recommended for users transforming from GDA94 coordinates derived from CORS | 2D
Conformal + Distortion grid | Appropriate for users transforming GDA94 coordinates derived from survey marks (e.g. SCIMS or SCIMS-localised CORS control). | 2D
Courtesy of Alex Woods, DELWP
www.sli.do #AGRS

## Slide 33: EPSG Codes
www.sli.do #AGRS
Update accuracy of GDA94-WGS84(generic) EPSG code (1150) from 1 m to 3 m
Introduction of GDA94-GDA2020 EPSG codes
Introduction of GDA2020-ITRF2014 EPSG code (8049)

## Slide 34: GDA94 – GDA2020 Transformation Service
http://positioning.fsdf.org.au/
www.sli.do #AGRS

## Slide 35
https://github.com/icsm-au/DatumSpreadsheets
www.sli.do #AGRS

## Slide 36: MGA94 to MGA2020
MGA94 to GDA94 (conversion: Krueger equations)
GDA94 to GDA2020 (transformation)
GDA2020 to MGA2020 (conversion: Krueger equations)
See GDA2020 Technical Manual for details and examples to perform these conversions and transformations
www.sli.do #AGRS

## Slide 37: Supporting GDA2020 since 9 February 2019
www.sli.do #AGRS

## Slide 38: GNSS CORS supporting GDA2020
GNSS CORS are now operating using GDA2020 coordinates
  CORS Networks will continue to support both GDA94 and GDA2020 real-time services
  There is currently no sunset date for GDA94
  RINEX and post processing products are typically GDA2020 by default (though they can be transformed easily)
  Users should consult their hardware or software supplier for further information
Courtesy of Hayden Asmussen, DELWP
www.sli.do #AGRS

## Slide 39: GDA2020 compliant vs GDA2020 compatible
GDA2020 Compliant Products
Are based on positions measured or calculated directly from coordinated positions that are traceable to the National Measurement (Recognized-Value Standard of Measurement of Position) Determination 2017.
Use algorithms that can produce the same results as the Geocentric Datum of Australia 2020 Technical Manual examples and sample data and the GDA94 – GDA2020 Online Transformation Service, within the limits of position uncertainties required by the product, and as documented by the product.
GDA2020 Compatible Products
Use a position uncertainty such that the difference between the datum used and GDA2020 is insignificant.
Contain support material consistent with the technical requirements set out in the Geocentric Datum of Australia 2020 Technical Manual and state the datum or reference frame being used or transformation algorithms used in preparing the product.

## Slide 40: GDA2020 Fact Sheets
https://www.icsm.gov.au/datum/gda2020-fact-sheets
www.sli.do #AGRS

## Slide 41: AUSGeoid09 (GDA94) vs AUSGeoid2020 (GDA2020)
GDA94 ellipsoidal height (603.346 m)
AUSGeoid09 value (15.850 m)
AHD
GDA94 (ITRF92)
GDA2020 (ITRF2014)
GDA2020 ellipsoidal height (603.249 m)
AUSGeoid2020 value (15.736 m)
terrain
p
(0.097 m)
www.sli.do #AGRS

## Slide 42: Connect with us
ICSM [http://www.icsm.gov.au]
ICSM-PCG Slack [http://cutt.ly/join-pcg-slack]
GDA Modernisation Implementation Working Group
GDA2020 Forum [https://www.icsm.gov.au/datum/gda2020-forum]
GitHub – Geoscience Australia Geodesy Python software [https://github.com/GeoscienceAustralia/GeodePy]
GitHub – ICSM Australian Geospatial Reference System tools and software [https://github.com/icsm-au]
GeodesyML [http://www.geodesyml.org/]
Twitter - Nicholas Brown [@nich0lasbr0wn] - Chair of PCG
Email geodesy@ga.gov.au
www.sli.do #AGRS

## Slide 43
www.sli.do #AGRS
www.sli.do
#AGRS

## Slide 44
Australian Geospatial Reference System
Webinar Series
Webinar 2: Geocentric Datum of Australia 2020
Nicholas Brown
Director of National Geodesy
Geoscience Australia
Chair of ICSM Permanent Committee on Geodesy
@nich0lasbr0wn