## Slide 1: How to prepare your metadata for upgrades to Australian Geospatial Reference System
Irina Bastrakova
ANZLIC/ICSM Metadata Working Group Meeting No 5, Canberra
28-29 October 2019

## Slide 2: Upgrades to Australian Geospatial Reference System
Providers and users of the spatial data needs to be aware of upgrades being made to the Australian Geospatial Reference System for the:
  Geocentric Datum of Australia 2020 (GDA2020)
  Australian Terrestrial Reference Frame (ATRF)
  Australian Vertical Working Surface (AVWS)
For more information visit https://www.icsm.gov.au/upgrades-australian-geospatial-reference-system

## Slide 3: Geocentric Datum of Australia 2020 (GDA2020)
The Geocentric Datum of Australia 2020 (GDA2020) is a static datum – just like GDA94
A ‘static’ datum means that the positions of features (e.g. roads, buildings), do not change over time despite the ongoing changes in the Earth’s surface
The upgrade to GDA2020 is to ensure spatial data can be more closely aligned to positions observed using Global Navigation Satellite System (e.g. GPS)
Changing to the GDA 2020 is beneficial for many applications where it is easier if the coordinates of features do not change (e.g. a major road development project)
Australia will move 1.8 meters north-east from 1994 by 2020
Adopting GDA2020, users will be able to benefit from modern positioning technology
GDA2020 is available for use now
Users can transform between GDA94 and GDA2020 using transformation parameters or grids

## Slide 4: Australian Terrestrial Reference Frame (ATRF)
The Australian Terrestrial Reference Frame (ATRF) is a time dependent reference frame
A ‘time-dependent reference frame/earth fixed’ means that positions of features change with time due to plate tectonic motion
GPS operates in a time-dependent reference frame
ATRF coordinates change with time as the Australian plate moves
A user can choose to use either GDA2020 or ATRF depending on their requirements
Users of ATRF are expected to be predominantly from the Intelligent Transport Services (e.g. autonomous vehicles) and Location Based Services (e.g. mobile applications)
ATRF will be available for use from 1 January 2020.

## Slide 5: Australian Vertical Working Surface (AVWS)
The Australian Vertical Working Surface (AVWS) is a new reference surface for heights in Australia free of the bias and distortion in Australian Height Datum (AHD)
AVWS heights can be computed directly from GNSS with accuracy of 4-8 cm
AVWS will be available for use from 1 January 2020

## Slide 6: The ISO 19115-1 and upgrades to AGRF
Metadata is an important component of the puzzle helping to understand and correctly apply the data.
The ISO 19115-1 contains a number of classes and elements record information which help to store information related to:
  upgrades to AGRF
  history of data transformation
Beyond metadata, information about data temporal extents, reference systems, its accuracy, etc. should be recorded against each measured observation in the dataset
  In particular, if a dataset has a wide variation of individual data observations taken at different accuracies and over a long time period.

## Slide 7
Class | Element | Definition | Comments
Reference System |  | Information about reference system | The Reference system enables ability for users to record information about spatial (horizontal and vertical) datums, projections and/or temporal systems for spatial, temporal or spatiotemporal datasets, including the code, authority and URL links describing Reference Systems
 | Reference System Identifier | Identifier for reference system | Specify the code, authority and URL of this authority e.g. reference to the Geodetic CRS for GDA2020, geographic 2D will be recorded as EPSG:7844, EPSG; http://www.epsg-registry.org. Realisation Epoch is recorded as part of CRS
 | Reference System Type | Type of the reference system used | Specify what reference system type the identifier belongs to: temporal, vertical, etc. e.g. the type of example above will be ‘geodeticGeographic2D
Temporal Extent |  | Provides temporal component of the extent of the referring object | Recording the time of observation is important to propagate coordinates back and forward through time for the Australian Terrestrial Reference Frame (ATRF) .Time period covered by the content of the resource (e.g. when data was collected or observed). Can be represented as a single datetime or a range (start and end datetime).
Lineage |  | Information about the events or source data used in constructing the data or lack of knowledge about them | Record history of the data lifecycle
 | Statement | General explanation of the data producer’s knowledge about the data history | Record of history of data generation or transformation, including accuracy/uncertainty of data
 | Process steps | Information about an event or transformation in the life of data including the process used to maintain data | Record procedure of data generation or transformation
Interim Solution: ISO 19115-1 classes and elements that can be used to record information relevant to upgrades to AGRF

## Slide 8: Open Discussion
Limitations of current standard:
  Data accuracy/uncertainty
  Types of date/time
ISO 19115-2:2019 – can it be used to capture data accuracy, transformation, epochs, etc.
Mandatory/optional elements
Recording provenance of data transformation
  Example: record of multiple epochs of data transformations
    1) E.g. Observe data: ATRFxxxx @Coordinate Epoch, observed at 20191021;
    Coordinate Epoch = Observation Epoch at this point.
    2) E.g. Propagate data: ATRFxxxx @anyCoordinateEpoch, observed at 20191021
    3) E.g. Transform data: GDA2020 @2020.0 (implicitly), observed at 20191021
    4) E.g. Transform data: ITRFxxxx @anyCoordinateEpoch, observed at 20191021
Other ISO standards